## Slide 1: Computer Networking
Network Model
Chapter 2

## Slide 2: Protocol Layering
Protocol: The rules that the sender, receiver and all intermediate devices follow to communicate effectively
Simple communication  Simple protocol
Complex communication  Protocol layering
Computer networks are complex systems
  Tasks involve varieties of hardware and software components, and protocols
Networking task is divided into several subtasks, or layers

## Slide 3: Real World Example
Communication between managers of two companies
Communicate

## Slide 4: What Actually happens
Communication takes place thru many layers
Logical communication
Secretary: types a letter
Delivery boy: drops the letter
Secretary: reads and reports the message
Delivery boy: takes the letter
Post office:
Processes and routes the letter
Postal truck

## Slide 5: Layer Model
Layer N uses services provided by Layer N-1
Layer N
Layer N
Using services
Providing services
Logical communication path
HOST A
HOST B
Layer N-2
Layer N-2
Layer N-1
Layer N-1
Virtual Communication System
Layer N protocol

## Slide 6: Why Layers?
Guidelines for protocol developments
  Reference model
Modularity
  Eases maintenance and updating of systems
  A change in one layer is transparent to the rest
It allows us to separate the services from the implementation.

## Slide 7: Two Principles of Protocol Layering
Bidirectional communication.
The objects under each layer at both sites should be identical.

## Slide 8: Internet Layer Model: TCP/IP Protocol Suite
The Internet Protocol Stack
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
User
Transmission Medium
Hardware
Software

## Slide 9: Application Layer
The only layer to interact with user
Responsible for providing services to the user
SMTP
HTTP
FTP
SMTP
HTTP
FTP
Data
Data
H5
Application Layer
to Transport
from Transport
Data
H5
Data
Logical communication

## Slide 10: Transport Layer
Duties/services
  Port addressing
  Segmentation and reassembly
  Connection control
  Flow control (end-to-end)
  Error control (end-to-end)
Responsible for delivery of a message from one process to another

## Slide 11: Transport Layer
Transport Layer
Data
Data1
Data2
Data3
H4
H4
H4
to Network
Data
Data1
Data2
Data3
H4
H4
H4
from Network
(segments)
Process
Process
…
Process
Process
…
PORT #
PORT #

## Slide 12: Network Layer
Duties/services
  Logical addressing
  Routing
Responsible for the delivery of packets from the original source to the destination

## Slide 13: Network Layer
Network Layer
Data
from Transport
to Data Link
Data
to Transport
from Data Link
Data
H3
Data
H3
(packet)

## Slide 14: Network Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Router
Data
1.1
5.7
1.1, 1.2, 6.1, 5.7, ... are logical addresses
R1
R3
R2

## Slide 15: Data Link Layer
Duties/services
  Framing
  Physical addressing
  Flow control (hop-to-hop)
  Error control (hop-to-hop)
  Access control
Responsible for transmitting frames from one node to the next

## Slide 16: Data Link Layer
Data Link Layer
Data
from Network
to Physical
Data
to Network
from Physical
Data
H2
Data
H2
(frame)
T2
T2

## Slide 17: Data Link Layer
3B
A3, 3B, 82, 9F, ... are physical addresses
9F
82
A3
Data
9F
T2
A3
Data
H2

## Slide 18: Data Link Layer
Network 1
Network 6
Network 5
1.1
1.2
6.6
6.1
6.3
5.7
5.2
Network 3
3.8
3.3
Data
1.1
5.7
97
32
25
79
62
54
74
12
88
Data
1.1
5.7
25
97
Data
1.1
5.7
62
79
Data
1.1
5.7
74
54
R1
R3
R2

## Slide 19: Physical Layer
Duties/services
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate (transmission rate)
  Synchronization of bits
Responsible for transmitting individual bits from one node to the next

## Slide 20: Physical Layer
Physical Layer
Data
from Data Link
to Data Link
Data
01001011
01001011
Transmission medium
(bits)

## Slide 21: The Big Picture
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111011010101001010101001
L5 data
H5
L4 data
H4
L3 data
H3
L2 data
T2
H2
0111010101010010101010101
5
4
3
2
1
5
4
3
2
1
Transmission medium

## Slide 22: Internet Model
Network
D.L.
P.L.
D.L.
P.L.
Network
D.L.
P.L.
D.L.
P.L.
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Transmission medium
sender
router
router
receiver

## Slide 23: Internet Model

## Slide 24: Protocol Suites
A set of protocols must be constructed
  to ensure that the resulting communication system is complete and efficient
Each protocol should handle a part of communication not handled by other protocols
How can we guarantee that protocols work well together?
  Instead of creating each protocol in isolation, protocols are designed in complete, cooperative sets called suites or families
Notes: 24

## Slide 25: Internet Protocol Suite
Layer | Protocols
Application | HTTP, FTP, Telnet, SSH, SMTP, DNS, SNMP, IGMP, …
Transport | TCP, UDP, SCTP, ...
Network | IP (IPv4), IPv6, ICMP, IGMP, ARP, RARP, ...
Data Link | Ethernet, Wi-Fi, PPP, ...
Physical | RS-232, DSL, 10Base-T, ...

## Slide 26: Addresses in TCP/IP
Notes: 26

## Slide 27: Addressing in TCP/IP
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Specific Addresses
Port Addresses
Logical Addresses
Physical Addresses
Addresses
Packet Names
Message
Datagram/Packet
Segment/User
Datagram
Frame
Bits
Layers

## Slide 28: Physical Addresses
Notes: 28

## Slide 29: Logical/IP Addresses
Notes: 29

## Slide 30: Port Addresses
Notes: 30

## Slide 31: OSI Model
OSI – Open Systems Interconnection
Developed by the International Standards Organizations (ISO)
Two additional layers
  Presentation layer
  Session layer
7.Application Layer
6.Presentation Layer
5.Session Layer
4.Transport Layer
3.Network Layer
2.Data Link Layer
1.Physical Layer
User
Transmission Medium

## Slide 32: Session Layer
Duties/services
  Interaction management
     Simplex, half-duplex, full-duplex
  Session recovery
Responsible for establishing, managing and terminating connections between applications

## Slide 33: Presentation Layer
Duties/services
  Data translation
  Encryption
  Decryption
  Compression
Responsible for handling differences in data representation to applications

## Slide 34: OSI Layers in Real World
transmission medium
Reads the message
Summarizes or translates letter
Opens letter
Withdraws letter from mailbox
Checks address and sorts letter
Unpacks packages
Unloads from truck
Handwrites a message
7.Manager
Prepares final version
6.Assistant
Provides address and packs letter
5.Secretary
Delivers letter to post office
4.Driver
Checks address and sorts letter
3.Postal staff
Packs letters for certain directions
2.Postal staff
Loads on truck
1.Postal staff
Pictures from Wikipedia

## Slide 35: Lack of OSI Model’s Success
Costly
Some of layers were never fully defined
Performance
Few Slides taken and modified from Chaiporn Jaikaeo